## Slide 1: Satellite Communication Systems

## Slide 2: 07 Space Segment

## Slide 3: The space segment in satellite communication consists of the satellites themselves and the communication links that facilitate data transmission between the satellite and ground stations
The three functions of a communications system are receiving commands from Earth (uplink), transmitting data down to Earth (downlink) and transmitting or receiving information from another satellite (crosslink or inter-satellite link).
Satellite: the main component hosting all hardware and software systems as the central components, orbiting the Earth to facilitate communication over long distances.
Ground Station: Ground stations are terrestrial facilities equipped with antennas and transceivers that communicate with satellites.

## Slide 4: Satellite Components
Communication modules: antenna and repeater are called payload.
Modules that support the payload such as electric power, propulsion, telemetry, tracking, etc. are called platform.

## Slide 5: Radiation Influences
Objects in space receive light (and heat) from the sun, but they also radiate heat into the blackness of space. Thermal equilibrium must be obtained.
There are 3 ways to transfer heat, conduction, convection, and radiation. In the vacuum of space, there is no air or other material to conduct or convect heat away from the satellite. Instead, satellites lose heat by emitting infrared radiation.
Satellite temperature highly depends on the payload and can be achieved through passive means (i.e. by radiation) or in case very low temperatures are needed (e.g. radio telescope), coolant (such as liquid helium) is present on-board.
Notes: Kondukcija (vođenje topline) - dvaju tijela u dodiru.
Konvekcija (strujanje topline) strujanje fluida (tekućina i plinova).
Radijacija (toplinsko zračenje) putem elektromagnetskog zračenja.

## Slide 6: Satellites rely on antennas for communication, telemetry, data transmission, and Earth observation
Unlike terrestrial antennas, satellite antennas operate in the vacuum of space, demanding precise engineering and performance.
Satellite antennas must fulfill the following requirements:
High gain for long-distance communication.
Beam control, either fixed or steerable.
Broadband capacity for high-throughput missions.
Compact & lightweight for launch compatibility.
Reliability to survive space environments (vacuum, radiation, temperature shifts).
Source: What Type of Antennas Are Used on Satellites? | Satellite Antenna Guide

## Slide 7: The subsystem, which provides the connecting link between transmitting and receiving antennas of a satellite is known as Transponder
Electronic device for receiving and transmitting signals
It is used to receive signal from one or more earth satellite stations and send the signals back to one or more receiving satellite earth stations.
Most common Heterodyne transponder.
Historically, only RF operations were performed usually using bent-pipe transponders and are still popular due to cost and simplicity. Recently regenerative transponders are being more frequently used.
Duplexer
LNA
Carrier processor
HPA
Satellite antenna
Notes: https://paradigma-tech.com/ka-band-transponder/

## Slide 8: Transponder structure
Duplexer is a two-way microwave gate. It receives uplink signal from the satellite antenna and transmits downlink signal to the satellite antenna.
Low Noise Amplifier (LNA) amplifies the weak received signal.
Carrier Processor performs the frequency down conversion of received signal (uplink). This block determines the type of transponder.
Power Amplifier amplifies the signal power to the required level.
Input Filter
LNA
∿
Local oscillator
Input Multiplexer
Output
Multiplexer
High Power
Amplifiers
Down Converter
Satellite Repeater
Transmitting Earth station
Receiving Earth station
Band Pass Filter
Demodulator
LNA
∿
Local oscillator
Amplifier
High Power Amplifier (HPA)
RF Frequency Mixer
High Gain Receiving Antenna on Satellite
Band Pass Filter
Processing
Modulator
Amplifier
∿
Local oscillator
High Gain Transmitting Antenna on Satellite
RF Frequency Mixer
Regenerative
Bent pipe

## Slide 9: Main part of transmitter is the power amplifier
Amplifiers work with signals from 0.3GHz to 300GHz (1m-1mm wavelength)
RF power amplifiers can be manufactured using a solid-state device like LDMOS, GaN, etc. or using vacuum tubes.
Types of amplifiers: Klystron, Magnetron, Traveling Wave Tubes, Crossed Field Amplifiers, Maser, Klystrons, Velocity modulations, Two cavity KlystronsT…
For usage where comparatively lower power amplification is required, Solid State Power Amplifiers are generally considered. They are further sub-divided into several classes, each with specific characteristics. SSP amplifiers are commonly seen in the LNAs.
For applications where considerably higher amplification is required, vacuum tubes are considered, for example Travelling wave tube
TWT (Traveling Wave Tube) amplifiers are generally very commonly used in RF communication space due to high amplification, low noise, wide bandwidth and high operating frequencies.

## Slide 10: Transponder
Functions | TWTA |  | SSPA | 
All units have the same linearity, intermodulation, and spectral regrowth performance |  |  |  | 
 | Advantages | Disadvantages | Advantages | Disadvantages
Linearity and Intermodulation Distortion | TWTA and GaN SSPA are equal |  | GaN SSPA and TWTA are equal | 
Available Output Power | Higher available output power and at higher frequencies |  |  | 
Efficiency of Operation, i.e. AC Power Consumption | More efficient in the back-off state | High Voltage = 10.000+V |  | High Currents = 100+A
Size and Weight | TWTA packages including power supplies are smaller and weigh less |  | Basic RF modules are but the power supply and required heat sinks make the overall package larger | 
Heat Dissipation | TWTA power distributed over a relatively large area, making heat sinking a less challenging task |  |  | Power FETs dissipate large amounts of power at a concentrated point. Heat dissipation is currently one of the most challenging problems in SSPA design
Reliability | Many years of reliable operation on spacecrafts/satellites | Limited life from 40,000 to 100,000 hours of continuous operation | Theoretically could have MTBFs greater than 1,000,000 hours | Power Supply reliability is a known SSPA problem
Temperature Stability | TWTs are very stable over temperature | Solid state driver amplifiers need to be temperature compensated |  | SSPAs and driver amplifiers need to be temperature compensated
Noise Power |  |  | 10 dBm better than TWT | 
Harmonics |  |  | 10 dBc better than TWT | 
Reliability vs. Temperature | Operate up to 85 degrees C |  |  | Operate up to 65 degrees C

## Slide 11: High Throughput Satellites (HTS) offer significantly enhanced throughput compared to conventional Fixed Satellite Service (FSS)
HTS operate in Ka-band or Ku-band frequencies and offer significantly higher amount of data compared to traditional satellites (Tbps vs Gbps).
Challenges of HTS
Spectrum Availability: Securing sufficient spectrum for high data rates and capacity can be challenging due to spectrum congestion and regulatory constraints.
Interference: Coordinating with other satellite systems to avoid interference is crucial, especially in densely populated satellite orbits.
Ground Infrastructure: Establishing a robust ground infrastructure to support HTS operations, including gateway stations and beam hopping support, requires significant investment and coordination.
Cost: HTS development and maintenance can be expensive, including satellite construction, launch, and ground infrastructure costs.
The term ‘throughput’ refers to the data transfer capacity, and HTS achieves a substantial increase in this capacity within the same orbital spectrum, ranging from two to more than 100 times that of traditional FSS

## Slide 12: Very High Throughput Satellites (VHTS), the latest batch of post-HTS satellites are characterized by flexibility, power, and speeds of 200 Gbps
Under development
They are connected to the ground segment by optical technologies (optical feeder links).
Inter-satellite links (ISL) are used to efficiently route data streams over the satellite network.
Beam Hopping
  Adapts to the varying demand in the course of the day
  Facilitates the adaptation of a satellite to new services with a different workload
  Supports coverage for locally fluctuating data traffic from mobile users

## Slide 13: NG Satellites - Flexible Payloads
DTP Key performances:
Very wide digitalized bandwidth (many hundreds of MHz)
Many tens of GHz of full capacity
Cost decreases in Mass/consumption/volume per GHz
Digital Transparent Processor (DTP) is currently a key technology for telecommunications payload: The ability to sample and digitally onboard process data flows with increasing data rates.

## Slide 14: Beam coverage is a critical aspect of satellite communications, determining the extent and quality of the signal received on Earth
Single beam coverage
Multi-beam coverage
Beam coverage refers to the area on the Earth's surface where a satellite's signal is strong enough to be received and decoded by a user terminal. Simplified, Beam coverage is defined by the footprint of a satellite's antenna beam on the Earth's surface. Beam coverage directly impacts the availability, reliability, and capacity of satellite-based services, including telecommunications, broadcasting, and navigation.
There are several types of beam coverage, each with its own advantages and disadvantages (we will mention only two):

## Slide 15: Some of key Challenges related to the space segment
Signal latency: Especially in geostationary satellites (GEO), where the long distance (~36,000 km) introduces noticeable delay in communication.
Bandwidth limitations: Limited spectrum availability restricts data throughput, making it difficult to meet growing demand.
Interference and jamming: Signals are vulnerable to atmospheric disturbances, intentional jamming, and cross‑satellite interference.
Orbital congestion: Increasing numbers of satellites, especially in LEO constellations, raise risks of collisions and space debris.
Power and thermal constraints: Satellites rely on solar panels and batteries, facing challenges in energy efficiency and heat management

## Slide 16: Thank you