## Slide 1: Satellite Communication Systems

## Slide 2: 08 Ground Segment

## Slide 3: A ground segment consists of all the ground-based elements of a space system used by operators and support personnel
Source:
The European Space Agency - Photo: ©ESA
ESA - Redu facilities
Ground segment refers to the collection of ground-based hardware and software components used to support the operation, communication, and control of satellites orbiting the Earth.
Key components are:
Ground Stations
They consist of antennas, transceivers, amplifiers, and other related equipment that enable the reception and transmission of signals to and from satellites.
Tracking, Telemetry, and Command
The TT&C system is responsible for monitoring and controlling the satellite’s health, position, and operational status.
Mission Control Center
The MCC is the hub of satellite operations, where personnel monitor and control all aspects of the satellite’s mission
Data Processing and Distribution Centers
These centers process, store, and distribute the data collected by the satellites to end-users or other organizations.
User Terminals
User terminals are the end-point devices that receive and transmit data from and to the satellites.
Network Operations Center
The NOC oversees the overall health and performance of the ground segment’s communication networks.
Backup and Redundancy Systems
These systems may involve duplicated hardware, backup power sources, and alternate communication links that can be activated in case of an emergency or system failure.

## Slide 4: The backbone of satellite networks is the ground segment
Ground stations are vital for satellite operational success and data integrity.
Mission control centers oversee spacecraft telemetry and performance monitoring.
Integration and testing facilities ensure satellite system reliability and functionality.
Ground networks optimize connectivity and enable seamless data exchange in satellite networks.
Source: Ground segment - Wikipedia

## Slide 5: Ground stations are strategically located around the globe to provide continuous coverage and support to orbiting satellites
Source: 11.0 Ground Data Systems and Mission Operations - NASA
AWS Ground Station is a managed service that lets customers build ground segment architectures in the cloud to control their satellites, process satellite data, and scale satellite operations without having to worry about building or managing their own antenna infrastructure. Customers can stream satellite data from any of the AWS antennas to the Amazon Elastic Compute Cloud (EC2) for real-time processing or to directly store data in the Amazon Simple Storage Service (S3).
The baseline of Kongsberg Satellite Services AS (KSAT)’s 3.7-meter KSATLITE antennas provide X-band and S-band for downlink and S-band for uplink. KSAT operates over 100 KSATLITE antennas at 15+ ground station sites across the globe, supporting over 1.5 million passes in 2023 alone.

## Slide 6: When selecting a position for a ground station in a satellite communication system, several factors should be considered to ensure optimal functionality and communication efficiency
Terrain and Obstacles: The site should have a clear view of the sky to minimize signal interference caused by buildings, trees, or geographical features.
.
Elevation: Higher elevations provide better line of sight with satellites and reduce the likelihood of signal obstructions from surrounding structures or terrain.
Accessibility: Easy access to the site is crucial for maintenance and repairs. Additionally, good accessibility facilitates the installation of equipment and the delivery of supplies.
Environmental Factors: Local weather conditions, potential sources of electromagnetic interference, and adherence to zoning regulations play a significant role in determining the suitability of a site location for a ground station.
Properly positioning antennas is essential for maximizing signal strength and quality. Factors such as elevation, obstructions, and interference must be considered to optimize performance. Neglecting antenna placement can result in poor reception and communication issues.

## Slide 7: An example transmit and receive block diagram
Simplified, data must be modulated for transmission. Then only intended frequency range must be transmitted. Upconverter converts the intermediate frequency to transmission frequency which is then amplified and transmitted through the antenna.
On receiving sited, the process is reversed.

## Slide 8: Satellite antennas are essential for satellite communications as they play a crucial role in the transmission and reception of data, voice, and video signals
Antennas are crucial for both ground stations and satellites.
Ground station antennas transmit signals to satellites and receive signals from them.
General Figure of merit of Antenna is G/T
The G/T (Gain-to-Noise Temperature ratio) of an antenna is a critical figure of merit that measures its performance in receiving weak signals.
It is expressed in decibels per Kelvin (dB/K) and provides insight into the antenna's ability to amplify desired signals while minimizing noise.
G is the antenna gain in decibels at the receive frequency.
T is the system noise temperature in Kelvin (K)
Higher the G/T means better performance in detecting week signals, which is crucial for satellite communication
Satellite antennas in Prottes, Austria, Eviden Lab.
Antenna size usually is derived from its intended use and frequency at which it operates. VSAT antennas usually have diameter from 0.75 m to below 4m and are generally considered for general consumer use. HUBs usually have larger antennas with maximum diameter below 20m. Higher diameter antennas are usually for specialized use.

## Slide 9: Example of ASTRA 1N
Antenna
Antenna characteristics are determined by type of signal received
For Astra 1N, we have Ku band with EIRP of anywhere between 45dBW to 51dBW which would equate to need for parabolic antenna size from 90 to 55cm
~Dish size (with noise figure of 0.7dB)
EIRP [dBW] | Dish diameter [cm]
51 | 55
50 | 60
49 | 60
48 | 60
47 | 75
46 | 80
45 | 90
Astra 1N is part of Astra 1 constellation of four high-powered satellites at 19.2°E inclination which are owned and operated by SES. Constellation consists of Astra 1L, Astra 1KR, Astra 1M and Astra 1N, all providing services to Europe and North Africa.
Channel bandwidth is between 26MHz and 33MHz.
Downlink frequencies are around 10.7-12.75 GHz (both standard Ku-band and extended Ku-band) and uplink frequency is around from 12.7-18.1 GHz.

## Slide 10: ASTRA 1N example – Components on the receiving side
Antenna
LNB
converter
Satellite
Receiver / IDU
(Indoor Unit)
On the receiving side there is a LNB – Low-Noise Block Down converter connected to the parabolic antenna.
LNB converts the Ku band to a frequency range from 950 MHZ to 2150 MHz (L-Band).
LNB is further characterized by
  Gain – for this application, usual is from 50 dB to 70 dB
  Filters – usually LTE filters are applied
  Cross Pol. Isolation – usually between 22 dB and 25 dB (the higher the better)
  Noise figure – usually below 0.5dB (the lower the better)
  Return loss, L/O, required power supply…
Antenna characteristics are determined by type of signal received
For Astra 1N, we have Ku band with EIRP of anywhere between 45dBW to 51dBW which would equate to need for parabolic antenna size from 90 to 55cm
~Dish size (with noise figure of 0.7dB)
Called by few names, Receiver, IDU or Satellite Modem
It is the core processing component of the complete system, it performs
Conversion of modulated signals back into baseband digital signals (Demodulation function).
Recovery of the original transmitted data by decoding the modulated signal (Decoder function).
Some other functions, such as providing power for LNB, performing Error Correction, User interface,.
EIRP [dBW] | Dish diameter [cm]
51 | 55
50 | 60
49 | 60
48 | 60
47 | 75
46 | 80
45 | 90

## Slide 11: The geometry of a parabolic antenna is defined by its parabolic shape, which focuses incoming waves at a single point, maximizing gain and directivity
The parabolic shape ensures that all waves emanating from the focus reflect off the surface and travel parallel to the axis of the parabola. This property is essential for achieving high directivity and gain, as it allows the antenna to focus energy into a narrow beam.

## Slide 12: Antenna gain quantifies the ability of an antenna to focus energy in a particular direction, enhancing the signal strength in that direction
For transmitting antenna, the gain describes how well the antenna converts input power into radio waves headed in a specified direction.
For receiving antenna, the gain describes how well the antenna converts radio waves arriving from a specified direction into electrical power.
xyz are power density axes in watts per square meter.
R is the radiation pattern of a directive antenna, which radiates a maximum power density of S watts per square meter at some given distance from the antenna.
Riso is the radiation pattern of an isotropic antenna which radiates the same total power, and Siso is the power density it radiates.
Visualization of gain

## Slide 13: The radiation pattern of an antenna is a graphical representation that illustrates how the antenna radiates energy into space
Main Lobe: The direction in which the maximum radiation occurs. This indicates the antenna's directivity.
Side Lobes: Areas of lesser radiation that occur away from the main lobe. They can indicate unwanted radiation and affect performance.
Back Lobe: Radiation that occurs in the opposite direction of the main lobe, often minimized in well-designed antennas.

## Slide 14: Low-noise antennas are essential for receiving weak signals from satellites, where antenna noise temperature plays a critical role in overall system performance
Noise temperature is one way of expressing the level of available noise power introduced by a component or source.
Noise is everywhere, all attributing to the Antenna noise temperature, for example contributing factors are
  Sky noise is one of the contributing factors, especially in bands such as Ka or Ku due to atmospheric absorption
  Elevation (at lower elevations, antenna collects more noise due to the longer path signal takes through the atmosphere)
  Cosmic background radiation (~2.7K)
  Ground noise
  Weather
  Design – Feed, LNA…
  Frequency band – Higher frequencies suffer from attenuation due to atmospheric loss, lower frequencies (<3GHz) due to galactic sources
  Human made – vehicles, buildings, reflection, scattering..

## Slide 15: Regular maintenance of satellite antennas is crucial for ensuring optimal performance, preventing signal loss, and extending the lifespan of the equipment
Example: De-icing & De-hydrating
Ice on the antenna is the main reason for a weak signal during winter.
The antenna is heated with heaters from the rear side.
Temperature sensors determine when heating is needed
Waveguides must be de-hydrated in order to prevent moisture and thus degradation of the signal quality
and then electric current starts to flow through heaters.
Proper maintenance is vital to avoid disruptions caused by environmental factors, equipment wear, and misalignment. Regular checks can help identify issues before they escalate, ensuring continuous and reliable service.
Key Maintenance Practices:
Routine Inspections
Cleaning
Lubrication
Alignment Checks
Preventive Maintenance

## Slide 16: The Largest Antennas
Notes: Arecibo, Puerto Rico

## Slide 17: Utilizing a combination of Very Small Aperture Terminals (VSATs) in star or mesh configurations, ground networks employ advanced data transmission methods to facilitate seamless satellite connectivity
Small intelligent earth satellite stations working in a system with one larger HUB earth station and a satellite in GEO orbit.
Usable for broadcasters, banks, airplane companies, oil and gas industry, news gathering, telemedicine, etc...
Terminals can just receive signal, just send signal or both.
Users are arranged in star, mesh or point to point network.
VSAT networks can operate in any band, but are usually mostly used in Ku for consumer broadband and enterprises and in Ka band for high capacity broadband.
Very Small Aperture Terminals (VSATs)

## Slide 18: VSAT (Very Small Aperture Terminal) network architecture primarily utilizes two topologies: Star and Mesh, each designed to meet specific communication needs
Broadly, a VSAT network consists of VSAT terminals distributed across different regions on Earth and a Hub station located at one central place. Communication between the Hub station and VSAT terminals is carried out using RF frequencies in different bands (e.g., C band, Ku band) as per applications and regions of use.
In a Star-type VSAT network, all communications occur through the Hub station using multi-hop communication.
In a Mesh-type VSAT network, all communications occur directly between VSATs without the need for a central Hub station.

## Slide 19: Thank you